## Slide 1
OS32C-Vup2
Omron PLC Function Blocks
Micheal Paradiso

## Slide 2: Objective
To develop a simple effective method to integrate the new Measurement capabilities of the OS32C with an Omron PLC.
To do this we will develop function blocks that can be used in the PLC code to automatically configure the PLC to display the needed OS32C data.

## Slide 3: Simple ?? Effective??
This will enable the OEM or end user to quickly integrate this sensor into the PLC control system.
This will speed up development time because all the work will be done for them

## Slide 4: Function Blocks Information
The three function block parameters and operation information are below:
Measurement Configuration function block:
Users will use this function block to specify the data they want to receive from the scanner.
Scan angle : This input will be in degrees as it is entered into the FB. This will be the size of the wanted beam angle.
Start Beam Read angle location: This will be entered as degrees into the FB. This will be the start location/angle the PLC will start reading the scanner’s data.
PLC Memory write location: This will be the DM memory location the scanners range data will be written too.
Beam spread: This will be the number of beams to be used in rage data, 1=every beam, 2=every other beam 4= every forth beam, 8= every eight beam will be used, 16= every sixteenth beam.
This function block was designed to work with “Input Assembly 102 & 103, Output Assembly 113. This function block dose not set the “Range Repost Bit” in word 1 of the output assembly, this bit needs to be set to something other than zero before the scanner range date will be reported.
Object detection function block (for fixed applications):
This function block is to help users process the data they're receiving from the scanner.
1. the size of the object
2. the distance of the object
3. Number of items in the view
4. Center of the detected object
Navigation data function block:
1. Detect reflectors
2. Distance of location
3. Input parameters for detection: size, reflectivity (x times more reflective than background reflectivity)

## Slide 5: Measurement Configuration FB
The “Measurement Configuration” function block can be used to report the range data for any needed part of the 270 deg field view of the scanner. This function block enables you to select any start location and the size of the of the data to be reported. This also enable you to change this report data on the fly if needed.

## Slide 6: Measurement Configuration FB
1-Scan angle: This parameter is set in deg’s. 2 -270 deg, this will be the size of the bean spread in deg’s.
2- Start Beam Read angle location: This parameter is set in deg’s. 2 -270 deg This is the location at where the scan angle will start reading.
Both these two parameter work together in this function block. How they work is once you set the beam start location, the function block will start producing beam range data starting at that location and continue producing beam data for the size of the “scan angle”.
Be careful not to set the start location so the end point of the scan angle will exceed 270 deg, this will cause an error.
90 deg
90 deg
Notes: <number>

## Slide 7: Measurement Configuration FB
1-Beam Spread: This perameter can only have five setting 1,2,4,8 or 16. What this will do is set the number of beam that will be used in the scan angle. If it is set to it will use every beam, if set to 2 it will use every other, etc.

## Slide 8: Measurement Configuration FB
Input Assembly: This is the start DM location of the input assembly, this is entered as an DINT second word should be 0
Output Assembly: This is the start DM location of the output assembly, this is entered as an DINT second word should be 0
Out Beam Data: This is the start DM location where the calculated range data will be written too. The DM location size will change with beam angle & bean spread are changed.
Beam Angle size: This is the size of the data that will be ouputted by FB, this entered as deg from 2 deg to 268 deg.
Beam Start Loaction: Start location of range data read. 2 to 270 deg
Beam Spread: Number of beams to be used, 1,2,4,8,or 16

## Slide 9: Assembly & PLC DM Info
To find what assembly and the DM memory location of the scanner can be found in the “Network Configurator software.

## Slide 10: Measurement Data Report values:
1-Object Size in number of beams
2-Oject distance in mm/cm
3-Object signal strength